## Slide 1
ENG 6010 · Artificial Intelligence in Robotics · Readings 6
From Mode-2 to Mode-1
Planning with a learned world model, then distilling it into a fast policy
Mode-2 · think
Mode-1 · react
Gymnasium Pendulum-v1 · PyTorch · CPU only
LeCun (2022) · Diffusion World Model (2024) · DreamerV3 (2023)
t = 0
t = 40
t = 60
t = 100
CEM planner swinging the pole up from hanging down
Notes: This project turns the common idea of this week's four readings into running code: learn a model of the world, plan with it slowly (Mode-2), then compile those plans into a fast reflex policy (Mode-1). Everything runs on a laptop CPU with python main.py.

## Slide 2
THE RESULT IN ONE SLIDE
Mode-1 keeps the planner's skill at a fraction of its cost
430×
faster decisions: 0.096 ms for the policy vs 41.3 ms for the CEM planner
98%
of the planner's improvement over random play is kept by the distilled policy
15
imagined steps per plan, the same horizon as DreamerV3's imag_length
Returns over 15 unseen test episodes (3 seeds), higher is better:
Random −1172 Random-shooting MPC −187 CEM MPC −155 Distilled policy −173
ENG 6010 · Readings 6 · Mode-2 to Mode-1
2
Notes: Headline: the distilled policy decides about 430 times faster than the CEM planner it learned from and keeps 98 percent of the planner's gain over random play. The planner looks 15 steps ahead, the same imagination length DreamerV3 uses.

## Slide 3
BACKGROUND
Four readings, one idea: imagine in training, act fast
LeCun (2022)
A Path Towards Autonomous Machine Intelligence
Mode-2: plan with a world model and a fixed intrinsic cost, act, replan
Fig. 5: compile Mode-2 plans into a fast Mode-1 policy
Ding et al. (2024)
Diffusion World Model
One-step models compound error over long rollouts (Fig. 1.1)
Imagined rollouts only in training, so the deployed policy is fast
Hafner et al. (2023)
DreamerV3
Learn a world model from experience, train behaviour in short imagined rollouts
symlog makes regression targets robust
danijar/dreamerv3
Official code
imag_length: 15 became my planning horizon
symlog/symexp in nets.py; one configs.yaml became config.py
ENG 6010 · Readings 6 · Mode-2 to Mode-1
3
Notes: Each reading contributed one ingredient. LeCun gives the architecture and the Mode-1/Mode-2 vocabulary. The Diffusion World Model paper explains why long imagined rollouts are dangerous and why imagination should stay in training. DreamerV3 and its code give the 15-step horizon, symlog and the single config file.

## Slide 4
LECUN'S ARCHITECTURE → MY CODE
The same agent, run in two modes
MODE-2 · DELIBERATE 41.3 ms per decision
Observation s
[cos, sin, dθ/dt]
CEM planner
planner.py
World model
world_model.py
Intrinsic cost
cost.py
Execute a₀
then replan
imagine 15 steps × 300 plans
distil: BC + DAgger on planner labels
MODE-1 · REACTIVE 0.096 ms per decision
Observation s
[cos, sin, dθ/dt]
Policy π(s)
policy.py
Execute a
every step
one forward pass, no search
ENG 6010 · Readings 6 · Mode-2 to Mode-1
4
Notes: Top lane is LeCun's Mode-2: the planner proposes action sequences, the world model imagines what happens, the fixed intrinsic cost scores the imagined states, and only the first action is executed before replanning. That is Model-Predictive Control. The bottom lane is Mode-1: a small network trained on the planner's decisions, which is LeCun's Figure 5.

## Slide 5
THE ROBOT
Pendulum-v1: a small but real swing-up problem
Torque is limited to ±2 N·m, so the pole must be swung, not lifted
State
s = [cos θ, sin θ, θ̇], θ̇ ∈ [−8, 8] rad/s
Action
torque u ∈ [−2, 2] N·m, 20 Hz control (dt = 0.05 s)
Cost (negative reward)
θ² + 0.1·θ̇² + 0.001·u² (0 = upright and still)
Episode
200 steps. Random play: −1172. Good swing-up: about −120 to −240
ENG 6010 · Readings 6 · Mode-2 to Mode-1
5
Notes: Pendulum-v1 has a three-number state, one torque, and a reward that penalises angle, speed and effort. The motor is too weak to lift the pole directly, so a controller has to plan a swing, which makes it a real, if small, planning problem. The same cost formula is used by my planner as LeCun's intrinsic cost.

## Slide 6
HOW THE CODE WORKS
One command, six stages: python main.py
1
Collect data
collect_data.py
50 random episodes give 10,000 (s, a, s′, r) transitions, saved as .npz
2
Train world model
world_model.py
MLP predicts Δs = s′ − s from normalised (s, a)
3
Test compounding error
multi_step_error()
Open-loop rollouts, 1-30 steps, on held-out data
4
Mode-2: CEM MPC
planner.py
Search 15-step plans in the model, run the first action, replan
5
Mode-1: distil
policy.py
Behaviour cloning, then 4 DAgger iterations
6
Evaluate and plot
evaluate.py · plots.py
4 controllers, 15 episodes, return and ms per decision
3 seeds · fixed random seeds everywhere · 10.8 min on one CPU thread · all hyperparameters in config.py
ENG 6010 · Readings 6 · Mode-2 to Mode-1
6
Notes: main.py runs these six stages for each seed, then pools the results, makes every plot and writes summary.json. Stages one to four are the world model and Mode-2 side; five and six are Mode-1 and the comparison.

## Slide 7
STAGE 2 · WORLD MODEL
Learning the physics from 10,000 random transitions
world_model.py (simplified)
def predict(self, obs, act):
# one imagined step: s' = s + f(s, a)
x = (cat([obs, act]) - in_mean) / in_std
y = self.net(x) # 3 x 128 SiLU MLP
delta = y * out_std + out_mean
if self.use_symlog: # DreamerV3
delta = symexp(delta)
nxt = obs + delta
cs = unit_circle(nxt[:2]) # valid cos/sin
thdot = clip(nxt[2], -8, 8)
return cat([cs, thdot])
Predicting the change Δs gives a small, zero-centred target
Inputs and targets are standardised; statistics are stored inside the model
Optional --symlog flag: regress symlog(Δs), map back with symexp
0.00046
train MSE (normalised)
0.00053
validation MSE
Seed 0, after 60 epochs: no overfitting
ENG 6010 · Readings 6 · Mode-2 to Mode-1
7
Notes: The world model is a plain MLP that predicts the change in state. Two pieces of prior knowledge keep rollouts valid: cos and sin are put back on the unit circle and the speed is clipped like the simulator. The one-step fit is excellent, with train and validation losses almost equal.

## Slide 8
STAGE 3 · DIFFUSION WORLD MODEL, FIG. 1.1
Small one-step errors compound over the horizon
Chart: open-loop horizon (steps)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
Plain targets | 0.00434 | 0.00788 | 0.01115 | 0.01415 | 0.01695 | 0.01958 | 0.02214 | 0.0247 | 0.02739 | 0.0303 | 0.0335 | 0.03715 | 0.04137 | 0.04634 | 0.05223 | 0.05919 | 0.06739 | 0.07694 | 0.0879 | 0.1003 | 0.11426 | 0.12996 | 0.14718 | 0.16563 | 0.18511 | 0.20585 | 0.22867 | 0.25481 | 0.28548 | 0.32137
symlog targets | 0.00607 | 0.01012 | 0.0138 | 0.01724 | 0.02048 | 0.02359 | 0.02662 | 0.02963 | 0.03278 | 0.03623 | 0.04001 | 0.04433 | 0.04936 | 0.05523 | 0.06217 | 0.07033 | 0.07984 | 0.09072 | 0.10288 | 0.11617 | 0.13069 | 0.14661 | 0.16363 | 0.18144 | 0.19989 | 0.21917 | 0.2399 | 0.26305 | 0.2895 | 0.31948
×12
error after 15 steps vs 1 step
×74
error after 30 steps vs 1 step
Angle error 0.05° → 0.95° → 4.2°
At H = 15 the model is still within 1°, so MPC plans only that far and replans from real observations (DreamerV3's 15-step imagination).
ENG 6010 · Readings 6 · Mode-2 to Mode-1
8
Notes: Every step, the model is fed its own slightly wrong prediction, so the error grows faster than linearly: about 12 times larger after 15 steps and 74 times after 30. This is the compounding error the Diffusion World Model paper shows in Figure 1.1, and the reason DreamerV3 imagines only 15 steps. symlog did not help here because Pendulum's state changes are already small.

## Slide 9
STAGE 4 · MODE-2 = MODEL-PREDICTIVE CONTROL
The Cross-Entropy Method plans inside the learned model
1
Sample 300 torque sequences of length 15 from a Gaussian
2
Roll each one through the world model and add up the imagined cost
3
Keep the 30 cheapest (elites) and refit the Gaussian; repeat 4×
4
Execute only the first action, then replan from the new real state
19,200 imagined model steps per decision
planner.py (simplified)
def imagined_cost(model, obs, plans):
s = obs.expand(N, -1)
total = zeros(N)
for t in range(H): # H = 15
a = plans[:, t:t+1]
total += pendulum_cost(s, a)
s = model.predict(s, a) # imagine
return total + pendulum_cost(s, 0)
# LeCun Mode-2: execute first action,
# keep the rest as a warm start
action = mean[0]
self.mean = cat([mean[1:], zeros(1)])
ENG 6010 · Readings 6 · Mode-2 to Mode-1
9
Notes: CEM is a simple optimiser: sample, score in imagination, keep the best, refit, repeat. The planner never touches the simulator while thinking; it only uses the learned model and the fixed cost. Executing just the first action and replanning is what makes this MPC, and it limits the damage from compounding error.

## Slide 10
STAGE 5 · MODE-1, LECUN FIG. 5
DAgger turns the planner into a reflex
Behaviour cloning
Imitate the planner on its own 3 episodes
DAgger iteration
Let the policy drive; the planner labels every state it visits
Aggregate and retrain
600 → 3,000 labelled states, including recovery states
BC alone scored about −1550 on 2 of 3 seeds, worse than random. DAgger fixed it.
Chart: policy return
| BC | DAgger 1 | DAgger 2 | DAgger 3 | DAgger 4
Seed 0 | -1551.6 | -236.7 | -214.8 | -194.2 | -193.4
Seed 1 | -1549.3 | -74.9 | -74.9 | -74.6 | -74.3
Seed 2 | -907.2 | -1542.7 | -1417.7 | -155.6 | -152.1
CEM teacher | -155 | -155 | -155 | -155 | -155
ENG 6010 · Readings 6 · Mode-2 to Mode-1
10
Notes: Plain behaviour cloning only sees states where the expert is doing well, so the first mistake takes the policy somewhere it has never been trained on. DAgger asks the planner to label the states the policy actually visits, so it learns to recover. Seed 2 needed three iterations before it clicked.

## Slide 11
STAGE 6 · EVALUATION
Close to the planner's return at 1/430 of the decision time
Return, mean of 15 episodes (higher is better)
Chart: 
| Random | Rand. shoot | CEM MPC | Distilled
Return, mean of 15 episodes (higher is better) | -1171.6671 | -187.3566 | -155.0213 | -173.492
Milliseconds per decision (lower is faster)
Chart: 
| Random | Rand. shoot | CEM MPC | Distilled
Milliseconds per decision (lower is faster) | 0.0043 | 26.5656 | 41.2516 | 0.0959
± std: Random 259 Rand. shoot 96 CEM MPC 50 Distilled 75 · random-shooting gets the same 1,200-plan budget as CEM
ENG 6010 · Readings 6 · Mode-2 to Mode-1
11
Notes: On the same 15 unseen start states, CEM scores -155 and the distilled policy -173, against -1172 for random play. The policy needs 0.096 ms per decision against 41.3 ms for CEM. At 20 Hz control, CEM uses most of the 50 ms budget on one CPU thread; the policy uses a fraction of a percent.

## Slide 12
SEEING IT
Swing-up from hanging down, seed-0 controllers
Random
return −1663
Random-shooting MPC
return −496
CEM MPC
return −388
Distilled policy
return −576
t = 0
t = 24
t = 48
t = 72
t = 96
t = 124
t = 160
t = 198
Notes: All four start hanging straight down at rest, the hardest start. Random never gets up. Both planners and the distilled policy pump energy with a few swings and then balance; the policy takes a little longer, which is why its return on this one episode is lower than CEM's.

## Slide 13
BACK TO THE READINGS
What the readings claimed, and what my run showed
CLAIM
WHAT I OBSERVED
LeCun
Mode-2 can be compiled into a fast Mode-1 policy
430× faster, 98% of the planner's gain kept
Diffusion World Model
One-step models compound error; keep imagination in training
Error ×74 after 30 steps; the deployed policy never touches the model
DreamerV3
Short imagined rollouts (15 steps) are enough to learn behaviour
Angle error 0.95° at 15 steps, good enough to swing up
DreamerV3 code
symlog makes targets robust across domains
Slightly worse here: Pendulum's targets are already small (honest negative result)
ENG 6010 · Readings 6 · Mode-2 to Mode-1
13
Notes: Three of the four claims show up clearly even on this tiny problem. The symlog result is the honest exception: symlog exists to handle targets whose scale varies by orders of magnitude across domains, and a single well-normalised pendulum has no such problem.

## Slide 14
LESSONS AND LIMITATIONS
What surprised me, and what this experiment does not show
Surprises
Behaviour cloning alone was worse than random: the policy's own mistakes need labels
Retraining on CEM data (2 rounds) changed CEM's return by at most 0.1 point
symlog targets were slightly worse on this small, well-scaled problem
Random shooting with the same budget was close to CEM (−187 vs −155) but less consistent
Limitations
True 3-number state, not camera images (no representation learning)
Deterministic MLP: no uncertainty, no RSSM or diffusion model
Hand-written cost and no value function, so the planner sees only 0.75 s ahead
Imitation cannot beat its teacher; only 15 test episodes, and the ± ranges overlap
ENG 6010 · Readings 6 · Mode-2 to Mode-1
14
Notes: The biggest lesson was DAgger: the same compounding-error problem the world model has also hits the cloned policy. The main limitations are that I skip perception entirely and use a hand-written cost; DreamerV3 and DWM learn from pixels and learn a reward model and critic.

## Slide 15
TAKEAWAY
Think slowly while training. React quickly when deployed.
A learned world model plus a planner gives good behaviour; distilling that planner gives the same behaviour cheaply enough for a real-time robot.
reproduce
cd readings/Readings_6
pip install -r requirements.txt
python main.py # full run
python main.py --quick
github.com/CDJ7/ENG6010
readings/Readings_6
README · Program_Explanation · Results
Notes: That is the whole loop from LeCun's paper on a small scale: model, cost, plan, then compile the plan into a reflex. Everything shown is reproducible with one command from the repository.